## Slide 1
Model Institute of
Engineering & Technology
Course Name- Microprocessors
Course Code- COM 503
Lecture No- 1
Topic – Introduction to Microprocessors

## Slide 2: Course Outcomes
Course Outcomes | Description | Mapping with Program Outcomes and Program Specific Outcomes
CO 1 | Appreciate the architectural elements in a Microprocessor and their functionality. | PO[1,2,4] PSO[2,2]
CO 2 | Analyze, design, implement kand test various assembly language programs of moderate complexity. | PO[1,2,3] PSO[2,2]
CO 3 | Classify the instruction set of 8085 and 8086 microprocessors and distinguish the use of dfferent instructions and apply them in assembly level programming. | PO[1,2,3,4] PSO[1,2]
CO 4 | Appreciate the evolution of RISC and ARM processors and the improvements over older microprocessor architectures. | PO[1,2,3,4] PSO[1,2]
CO 5 | Appraise the architecture of advanced processor families | PO[1,2,3] PSO[2,2]

## Slide 3: Assessment and Evaluation Plan
Assessment Tools
Assignment
Sessionals
Attendance
External Exams
Evaluation
20 Marks
20 Marks
10 Marks
100 Marks

## Slide 4: Outcomes of Today’s Lecture
Introduction to Microprocessors
Evolution of Microprocessors

## Slide 5: Introduction to Microprocessor
A microprocessor is a programmable electronic chip that has computing and decision making capabilities similar to central processing unit of a computer.
Nowadays, microprocessor can be seen in almost all types of electronics devices like mobile phones, printers, washing machines etc.
A typical microprocessor consists of arithmetic and logic unit (ALU) in association with control unit to process the instruction execution.

## Slide 6
Almost all the microprocessors are based on the principle of store-program concept.
In store-program concept, programs or instructions are sequentially stored in the memory locations that are to be executed.
To do any task using a microprocessor, it is to be programmed by the user. So the programmer must have idea about its internal resources, features and supported instructions.
Each microprocessor has a set of instructions, a list which is provided by the microprocessor manufacturer.
The instruction set of a microprocessor is provided in two forms: binary machine code and mnemonics.

## Slide 7
Microprocessor communicates and operates in binary numbers 0 and 1.
The set of instructions in the form of binary patterns is called a machine language and it is difficult for us to understand.
Therefore, the binary patterns are given abbreviated names, called mnemonics, which forms the assembly language.
The conversion of assembly-level language into binary machine-level language is done by using an application called assembler

## Slide 8
Evolution of Microprocessors
4-bit Microprocessors The first microprocessor was introduced in 1971 by Intel Corp. It was named Intel 4004 as it was a 4 bit processor.
It was a processor on a single chip.
It could perform simple arithmetic and logic operations such as addition, subtraction, boolean AND and boolean OR.
It had a control unit capable of performing control functions like fetching an instruction from memory, decoding it, and generating control pulses to execute it.
It was able to operate on 4 bits of data at a time.
This first microprocessor was quite a success in industry. Soon other microprocessors were also introduced.
Intel introduced the enhanced version of 4004, the 4040.

## Slide 9
8-bit Microprocessors The first 8 bit microprocessor which could perform arithmetic and logic operations on 8 bit words was introduced in 1973 again by Intel.
This was Intel 8008 and was later followed by an improved version, Intel 8088. Some other 8 bit processors are Zilog-80 and Motorola M6800.
16-bit Microprocessors The 8-bit processors were followed by 16 bit processors. They are Intel 8086 and 80286.
32-bit Microprocessors The 32 bit microprocessors were introduced by several companies but the most popular one is Intel 80386

## Slide 10
Pentium Series Instead of 80586, Intel came out with a new processor namely Pentium processor.
Its performance is closer to RISC performance.
Pentium was followed by Pentium Pro CPU.
Pentium Pro allows multiple CPUs in a single system in order to achieve multiprocessing.
New instructions makes the Pentium III faster than high-end RISC CPUs.

## Slide 11: Thank You